OSHA FAQs: Confined Spaces in Construction

Confined spaces in the workplace can present physical and atmospheric hazards. Confined space hazards can be avoided if they are recognized and addressed prior to entering the confined space to perform work. OSHA has specific safety standards for construction work in confined spaces, which became effective on Aug. 3, 2015.

The current standard, Subpart AA of 29 CFR 1926, is intended to help protect construction workers from injury and death. The standard achieves this by eliminating and isolating hazards in confined spaces at construction sites. The standard is similar to safety standards that currently exist in other industries.

OSHA has provided these questions and answers to assist employers in protecting their workers while they are working in and around confined spaces in construction.

## What is a confined space?

A confined space has:

Limited means of entry and/or exit;

Is large enough for a worker to enter it; and

Is not intended for regular/continuous occupancy.

Examples include sewers, pits, crawl spaces, attics, boilers and many more.

## What is a permit-required confined space (permit space)?

A permit space is a confined space that may have a hazardous atmosphere, engulfment hazard or other serious hazard, such as exposed wiring, that can interfere with a worker’s ability to leave the space without assistance.

## Can anyone work in a permit space?

Only workers who have been assigned and trained to work in a permit space may do so. Additionally, before workers can enter a permit space, the employer has to write a permit that specifies what safety measures must be taken and who is allowed to go in.

## How do I know whether to follow the general industry rule or the construction confined space rule?

If you are doing construction work—such as building a new structure or upgrading an old one—then you must follow the construction confined space rule.

## I have been following the general industry rule. What is new or different about the construction rule?

There are five key differences from the construction rule and several areas where OSHA has clarified existing requirements. The five new requirements include:

- More detailed provisions requiring coordinated activities when there are multiple employers at the worksite (for more detail, see question below). This will ensure hazards are not introduced into a confined space by workers performing tasks outside of the space. An example would be a generator running near the entrance of a confined space causing a buildup of carbon monoxide within the space.

- Requiring a competent person to evaluate the work site and identify confined spaces, including permit spaces.

- Requiring continuous atmospheric monitoring whenever possible.

- Requiring continuous monitoring of engulfment hazards. For example, when workers are performing work in a storm sewer, a storm upstream from the workers could cause flash flooding. An electronic sensor or observer posted upstream from the work site could alert workers in the space at the first sign of the hazard, giving the workers time to evacuate the space safely.

- Allowing for the suspension of a permit, instead of cancellation, in the event of changes from the entry conditions listed on the permit or an unexpected event requiring evacuation of the space. The space must be returned to the entry conditions listed on the permit before re-entry.

In addition, OSHA has added provisions to the new rule that clarify existing requirements in the general industry standard. These include:

- Requiring that employers who direct workers to enter a space without using a complete permit system prevent workers’ exposure to physical hazards through the elimination of the hazards or isolation methods such as lockout/tagout.

- Requiring employers who are relying on local emergency services to arrange for responders to give the employer advance notice if they will be unable to respond for a period of time (because they are responding to another emergency, attending department-wide training, etc.).

- Requiring employers to provide training in languages and vocabulary that workers understand.

Finally, several terms have been added to the definitions for the construction rule, such as "entry employer" to describe the employer who directs workers to enter a space, and "entry rescue,” added to clarify the differences in the types of rescue employers can use.

## Why did OSHA believe that the former standard needed to be changed?

Previously the only requirement for confined spaces in construction was training. OSHA concluded this was inadequate, as injuries and fatalities continued to occur.

## How does the new final rule differ from the rules that previously applied to construction work performed in confined spaces?

The new rule requires employers to determine what kinds of spaces their workers are in, what hazards could be there, how those hazards should be made safe, what training workers should receive and how to rescue those workers if anything goes wrong.

## When did the current rule go into effect?

The current rule went into effect on Aug. 3, 2015.

## Do employers have to have a written confined space program?

Yes, if workers will enter permit spaces.

## Where can I find the final rule for confined spaces in construction?

The confined spaces standard can be found at www.osha.gov under 29 CFR Part 1926 Subpart AA - Confined Spaces in Construction. An electronic copy of the regulatory text can be accessed from OSHA's construction web page at final rule (PDF). The preamble to the final rule can also be found on OSHA's website under "Federal Register Notices" for May 4, 2015, or on the Federal Register website (https://www.federalregister.gov/) under Vol. 80, page 25365.

## How can I contact OSHA if I have questions about the final rule?

For compliance assistance regarding application of the final rule, contact: Directorate of Construction, Room N3468, OSHA, U.S. Department of Labor, 200 Constitution Avenue NW, Washington, DC 20210; telephone 202-693-2020 or fax 202-693-1689.

## Who is affected by Subpart AA?

All construction employers whose workers may be exposed to confined spaces hazards.

## Do I need to do anything if there are permit spaces at the worksite, but my employees will not need to enter the permit space?

Yes, you must take effective steps to prevent your employees from entering the space.

## If I hire a contractor (or subcontractor) to do work in a confined space, do I have any responsibilities?

Yes, controlling contractors and host employers must discuss spaces on the site and their hazards with entry employers and each other before and after entry.

## Tell me more about the conversations between host employers, controlling contactors and entry employers.

The rule makes the controlling contractor, rather than the host employer, the primary point of contact for information about permit spaces at the work site.

The host employer must provide information it has about permit spaces at the worksite to the controlling contractor, who then passes it on to the employers whose employees will enter the spaces (entry employers). Likewise, entry employers must give the controlling contractor information about their entry programs and any hazards they encounter in the space, and the controlling contractor passes that information on to other entry employers and back to the host. As mentioned above, the controlling contractor is also responsible for making sure employers outside of a space know not to create hazards in the space, and that entry employers working in a space at the same time do not create hazards for one another’s workers.

## What standard should I follow if my workers are doing construction AND general industry work in confined spaces?

An employer whose workers are engaged in both construction and general industry work in confined spaces will meet OSHA requirements if that employer meets the requirements of 29 CFR 1926 Subpart AA - Confined Spaces in Construction.

## Twenty-eight states and territories have their own OSHA-approved safety and health plans; will those states be required to adopt the new standard?

Yes, 22 states or territories currently operate their own OSHA-approved State Plans (covering private sector and state and local government employees), and five additional states and one territory (Connecticut, Illinois, New Jersey, New York and the Virgin Islands) operate plans that cover state and local government employees only. State Plans have and enforce their own occupational safety and health standards that are required to be at least as effective as OSHA's. Many State Plans adopt OSHA's standards identically, but some State Plans may have different or more stringent requirements.

## Where can I get more information about construction work in confined spaces?

More information is available at www.osha.gov.

## Does the Standard impose additional requirements on "permit-required confined spaces" beyond those imposed for "confined spaces"?

Yes. In fact, the vast majority of the Standard's requirements only apply to permit-required confined spaces, and attics, basements, and crawl spaces in a residential home will not typically trigger these requirements. Once the employer's competent person performs an initial evaluation and determines that a confined space does not require a permit (1926.1203(a)), the employer's only further obligations under the Standard are to have a competent person reevaluate the space and, if necessary, reclassify it as a permit-required confined space if changes in the use or configuration of the space occur that could increase the hazards or potential hazards to entrants or if the employer has any indication that the initial evaluation may have been inadequate (1926.1203(f)).

If the employer's competent person determines that the space is a permit-required confined space, the following provisions also apply: entry communication and coordination (1926.1203(h)), permit-required confined space program (1926.1204), permitting process (1926.1205), entry permit (1926.1206), training (1926.1207), duties of authorized entrants, attendants, and entry supervisors (1926.1208-1210), and rescue and emergency services (1926.1211).

“Competent person” means someone who is capable of identifying existing and predictable hazards in the surroundings or working conditions which are unsanitary, hazardous, or dangerous to employees, and who has the authorization to take prompt corrective measures to eliminate them (see 1926.1202 definition of "competent person").

Source: Occupational Safety and Health Administration

# Text boxes

Provided by Corkill Insurance Agency, Inc.

Confined Spaces:

Have limited means of entry and/or exit

Are large enough for a worker to enter

Are not intended for regular/continuous occupancy

Current Safety standard

Employers must determine:

The kinds of spaces their workers are in and what hazards exist there

How those hazards should be made safe

The training workers should receive

How to rescue workers if anything goes wrong

Links And Resources

OSHA Confined Spaces website

Complete OSHA FAQs on confined spaces in construction