### Reference Standard

Occupational Safety and Health Administration Material Handling and Storage, Subpart N including:

29 CFR 1910.179

### Purpose

This procedure establishes minimum criteria for the maintenance and use of overhead and gantry cranes

### Scope

This procedure applies to all of our company employees, all contractors and vendors performing work on company property, and all other individuals who are visiting or have business with our company. All cranes, including jibs, in our facility will comply with this procedure.

### Responsibilities

Management is responsible for development and review of this program. Management is also responsible for appropriate employee training.

Management and supervisors are responsible for enforcement of this program.

Employees shall comply with all procedures outlined in this policy.

Contractors and vendors shall comply with all procedures outlined in this policy.

### Definitions

Bridge: The part of the crane that carries the trolley and that is supported on both ends by a runway

Contractor:  A non-company employee being paid to perform work in our facility.

Crane: A machine for lifting and lowering a load and moving it horizontally, with an integral hoisting mechanism.

Gantry crane: A crane, similar to an overhead crane except that the bridge for carrying the trolley is rigidly supported by two or more legs on fixed rails or the runway.

Hoist: The device that lifts and lowers a load.

Load block: The assembly that is used as the attachment point for the load to be lifted.

Overhead crane: A crane with a moveable bridge carrying a movable or fixed hoisting mechanism and traveling overhead on a fixed runway structure, commonly called a bridge crane.

Runway: Rails or other framework on which the crane or trolley travels.

Trolley: The part of the crane that carries the hoist.

Vendor:  A non-company employee being paid to perform a service in our facility.

### Procedure

General Requirements

Crane and hoist modifications will only be made as follows:

- Using components supplied by or approved by the manufacturer;

- By a qualified engineer or the manufacturer;

- Modified cranes and hoists will be tested prior to being returned to service;

- All cranes and hoists will be marked with their rated load. Cranes will be marked on each side. The markings must be legible from the ground or floor;

- Each hoisting unit or load block must be marked with its rated load. The marking must be legible from the ground or floor;

- Only trained and authorized personnel are allowed to operate cranes and hoists;

- Crane operational areas will be located or marked so that no pedestrian or vehicle traffic routinely travels below the operational zone;

- All cranes with a power traveling mechanism that are not floor operated will be equipped with an automatic warning device to warn of bridge or trolley travel;

- Load hooks equipped with a safety catch will have the safety catch maintained and used at all times;

- Any crane or hoist that is found to be defective, damaged or not operating properly will be immediately removed from service; and

- At no time will the maximum rated load of a crane or hoist be exceeded.

### Inspections

Before Use Inspection

Prior to each use the crane operator will:

- Visually examine the crane and/or hoist to check for damage or missing parts including:

  - Hooks;

  - Chains and wire rope;

  - Hydraulic and/or pneumatic components, if present;

- Test all functional mechanisms for improper adjustment; and

- Test the function of the upper load limit switch;

Frequent Inspection

On a daily or monthly basis, a written inspection (see appendix A) will be conducted on:

- Hooks;

- Hoist chains and wire rope;

- Functional operation of all controls including limit switch; and

- Hydraulic and/or pneumatic components if present.

Periodic Inspection

On an annual basis a written inspection (see appendix B) will be conducted by a qualified contractor or an employee qualified by training and/or experience, and consisting of:

      - All elements listed under Frequent Inspection;

      - Deformed, cracked or corroded parts;

      - Loose bolts or rivets;

      - Cracked or worn sheaves or drums;

      - Excessive wear on brake system parts;

      - Load, wind and other indicators over their entire functional range;

      - Power plants including conformance to safety standards;

      - Excessive wear of chain drive sprockets;

      - Excessive chain stretch;

      - Electrical components;

      - Control components; and

      - All additional inspection elements as required by the crane or hoist manufacturer.

New or Altered Cranes

Prior to use new or modified cranes or hoists will be tested as follows:

      - Hoisting and lowering;

      - Trolley travel;

      - Bridge travel;

      - Limit switches, locking and safety devices;

      - The trip setting of the limit switches will be set to prevent contact of the of the hook or block with any part of the trolley; and

      - Rated load test with a know weight load not to exceed 125% of the rated load unless recommended by the manufacturer.

Cranes Not in Regular Service

        - Cranes that are idle for more than one month but less than six months will receive a Frequent Inspection as detailed above; and

        - Cranes that are idle for longer than 6 months will receive Periodic Inspection, as detailed above

### Crane and Hoist Operation

General Safety Requirements

- Read the manufacturer operator manual;

- Perform a visual inspection prior to each use;

- Only trained and authorized personnel can operate cranes and hoists;

- The operator is responsible for the safety of other personnel and material in the area;

- The operator must communicate crane and hoist movement to others in the area who may be affected. Sound the warning signal when approaching personnel;

- Cranes must not be used to lift personnel unless the crane is approved for that service and an approved personnel cage or basket is used;

- The maximum load rating must never be exceeded;

- Operators must check the path of their lift and set down point for obstructions and ensure the path is clear.

Operation

- The hoist chain or rope will be maintained free of kinks and knots and will not be wrapped around a load;

- Use only approved slings and lifting devices that have been inspected prior to use;

- The load must be attached by means of slings, chains or other lifting devices specifically designed for this purpose;

- The load must be secure and balanced with the hook at or near the balance point of the load;

- The sling, chains and other lifting devices must not be twisted upon themselves and/or with the hoist chain/rope;

- The operator must not place any body part under a suspended load;

- A suspended load must never be lifted over people;

- Loads will be moved with fluid motions avoiding sudden accelerations or stops;

- Side pulls are not allowed;

- Do not use limit switches to stop crane or hoist motion: use the controls;

- Test hoist breaks whenever lifting a load approaching maximum capacity: lift the load a few inches and stop motion with the brakes;

- If a load starts to slip or fall do not try to stop it: get to a safety area away from the drop zone;

- When two or more cranes are used in one lift a qualified person must be in charge of the operation;

- A load will not remain suspended without the crane operator being at the controls.

### Revision History Record:

| Revision Number | Section | Revised By | Description |
| --- | --- | --- | --- |
| 0 | NA | NA | Original document. |

Frequent Inspection

Crane and Hoist

Inspector: ____________________		Crane/Hoist/Both

Location/ID: __________________		Date: _____

(Check Pass 		X Fail		NA Not Applicable

Visual										Pass		Fail

- Crane attachment to structure

- Crane-condition of components

- Hoist attachment to crane/structure

- Trolley condition

- Hydraulic/pneumatic system components

- Hoist controls condition

- Hooks and hook latches

- Wire rope/chains

Operational								Pass		Fail

- Crane operation-all controls

- Hoist operation-all controls

- Upper limit device (no load, low steed)

Notes: ______________________________________________________

____________________________________________________________

____________________________________________________________

TAKE DEFECTIVE AND DAMAGED EQUIPMENT OUT OF SERVICE IMMEDIATELY

Periodic Inspection

Crane and Hoist

Inspector: ____________________		Crane/Hoist/Both

Location/ID: __________________		Date: _____

( Pass 		X Fail		NA = Not Applicable

Inspection*									Pass		Fail

- Deformed, cracked or corroded structure

- Loose, missing bolts, nuts, pins, rivets

- Cracks, excessive wear to sheaves and drums

- Worn, cracked or distorted parts such as: pins, wheels,
bearings, shafts, gears, rollers, locking and clamping 
devices, bumpers, stops

- Excessive wear of brake systems

- Excessive wear of chain drive sprockets 
and/or loose chain

- Deterioration of electronic components, buttons
and switches

- Operation of all sensors

- Operation of all limit switches

- Rope reeving: proper rope, attachment to drum,
number of raps, fit in the groove

- Hooks: cracks, twist, wear, bend/twist, throat opening

* All crane and hoist manufacturer standards and requirements must be followed during inspection.

Notes: ______________________________________________________

____________________________________________________________

____________________________________________________________

# Text boxes

Effective Date:

Revision #:

Cranes and Hoists Program												1

Cranes and Hoists Program												2

Cranes and Hoists Program											3

Cranes and Hoists Program												4

Cranes and Hoists Program											5

Cranes and Hoists Program											6