Re:  Safe-Tread Coating

Dan Hittenberger 									November 28, 2011

Acry-Tech Coatings, Inc.

3601 NE 5th Ave

Oakland Park, FL 33334

954-565-6001

www.acrytech.com

Dan,

Good to talk with you again. I want to extend my sincere gratitude to you and your staff for the excellent services you provided for us over the past several years.  We have been extremely satisfied with the performance of this product from start to finish.  We have purchased over 300 gallons your Safe-Tread coating to complete a multitude of projects.

The main project that we started to use the Safe-Tread on is our aluminum ramps that we are using for the portable classrooms at our schools.  I have attached several photos of before and after the coating process.  We have found that even though the aluminum ramps have grooves extruded into them, they still have a tendency to get slippery in wet and icy conditions, especially when you get to the top and change direction, causing staff and students to fall and get injured.  We used several ramps as test ramps utilizing several products on the market.

We decided that Safe-Tread was best product for our needs for several reasons.

- It was the easiest to apply; being single component and the grit texture already mixed in

- Thickest to fill the grooves; we needed to get above the grooves and create a non directional grip pattern.

- Durable; we have not had any wear off.

- Graffiti sprayed on it was removed with a high temperature pressure washer and the Safe-Tread stuck and      we didn’t have to recoat

- Also was most cost effective product available.  After we discovered that the Safe-Tread was exceeding our performance expectations we decided to coat all 125 ramps from top to bottom.

I have also used the Safe-Tread on a metal floor in a Walk-In Freezer.  The freezer was shut down to dry out.  The existing floor was prepped, coated and cured.  I guess time will tell how long this will last a in -20F freezer.

Another application was used on two flights of black slate steps in an elementary school that were slippery for the staff and students to use.  I prepped and coated the front 4” of the stair tread.  All of the Staff and students rave about how they perform as well as the color difference so the individual steps can be seen well.

Thanks again for the great product and service that you provide.

Jonathan Naill

Leadman – Paint/Floor

Building Services Department

Howard County Public School System, Maryland

410-313-7084